## Slide 1
Huawei FusionServer Configuration Guide （E9000）
2015-05

## Slide 2: Agenda
1
Click to add Title
Click to add Title
2
Huawei E9000 Server
Huawei E9000 IO System
Click to add Title
3
Configuration and Quotation Tool
Click to add Title
4
Demo

## Slide 3
E9000 Product Panorama
chassis
E9000 chassis
chassis
Computing node
Switch module
Switch module
Adopts the modular design for compute nodes, storage nodes, switch modules, fan modules, and power supply modules
12U high chassis, providing 8 full width or 16 half width slots
Support next 3 generation Intel processors
Support evolution of next decade network technology
Computing node
CX110
CX310
CX311
CX116
CX317
CX611
CX911/CX912
CH121
CH220
CH221
CH140
计算节点
CH222
CH240
CH242 V3
HW 2S Node
High density
Large memory
HW 2*2P Twin Node
Ultra high density
high performance
FW IO Expansion Node
Large memory
Strong expansion
FW IO Expansion Node
Large memory
Strong expansion
FW Storage Node
Large memory
Ultra large storage
FW 4P Node
High performance
Ultra large memory
FW 4P E7 v2 Node
High performance
Strong Expansion
Computing Node
GE
10GE/FCoE
IB FDR
Multi-plane Switch
8G/16G FC
Half-width 2-socket compute node
High density
Large memory
Half-width 2 x 2-socket twin compute nodes
Super high density
Outstanding computing capability
Full-width I/O expansion node
Large memory
Excellent expansion
Full-width storage expansion node
Large memory
Large storage
Full-width 4-socket compute node
Outstanding computing capability (E5-4600 v2 )
Large memory
Full-width 4-socket compute node
Outstanding computing capability (E7- v2/E7 v3 )
DDR3 /DDR4 DIMMS
Large memory/Large storage
CH121 V3
CH220 V3
CH140 V3
CH222 V3
CH240
CH242 V3
40GE
CX110
CX310
CX311
CX116
-pass through
CX317
-pass through
CX611
10GE+FC
CX912
CX111
CX210
8G FC
GE+FC
CX915
CX710
CX220
16G FC
Full-width storage expansion node
Large memory
Large storage
CH226 V3

## Slide 4
E9000 Chassis
E9000 chassis
specification
  Installed in a standard 19-inch rack, the E9000 is 12 U high. Its dimensions are: 530.2 mm x 442 mm x 840 mm (H x W x D)
  An E9000 chassis houses 16 half-width slots or 8 full-width slots
  Management modules support 1+1 redundancy and management protocols and interfaces such as IPMI 2.0, SOL, SSL, SSH, and web
  Supports up to 6 Platinum PSMs (AC 3000 W/DC 2500 W) in N+N/N+M redundancy with up to 95% efficiency under 50% load and supports dynamic management for PSMs in the hibernation state
  Provides 14 fan modules(3 groups) and every group supports single-fan failures
Half width slot
Full width slot
Management module
Switch
module
Power
supply module
Fan
module
Front view
Rear view
Chassis specification
2X
3X
4E
E4
E1
X3
X2

## Slide 5
CH140 product view
CH140 V3 Half Width Twin Computing Node
High performance : CH140 V3 support 4 maximum 145W E5-2600 v3 processors (18 cores at 2.3GHz)
Ultra-high computing density: One chassis supports 32*2P notes、64* Haswell EP 145W CPU, industry highest density
Single node maintenance
Highlights
Front view
Isometric view
Form factor | Half-width 2*2-socket computing node
Number of CPUs | 2*（1 or 2 ）
Processor model | E5-2600 v3 Series CPU
Number of DIMMs | Each 2S node provides 8 DDR4 DIMMs
Internal Storage | Each 2S node: 1 2.5 inch SSD/SAS/SATA 2 x Micro SD cards, supporting RAID 1
PCIe expansion | Each node provides 2 PCIe x8 MEZZ modules
Operating systems supported | Microsoft Windows Sever 2008 /2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX ……
Operating temperatures | 5℃-35℃
4DIMMs
1*2.5inch
HDD SSD
4DIMMs
2 x Micro SD slots
Notes: 448给个算法：14Gbps×32（两个连接器，32对serdes）
5.76T：16×36（32+4）

## Slide 6
Form factor | Half-width 2-socket computing node
Number of CPUs | 1 or 2
Processor model | Intel Xeon E5-2600 v3 Series CPU
Number of DIMMs | 24 DDR4 DIMMs, providing a maximum capacity of 1.5TB
Number of HDDs | 2 x 2.5” SSDs or SAS/SATA HDDs, supporting 2 x PCIe SSDs
RAID support | Support RAID 0 and 1
PCIe expansion | 2 PCIe x16 MEZZ modules 1 standard PCIe x8 full-height half-length card
Operating systems supported | Microsoft Windows Sever 2008/2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX
Operating temperatures | 5℃-40℃
Dimensions | 210 mm x 537.2mm x 60.46mm
CH121 product view
CH121 V3 Half Width Computing Node
Front view
Isometric view
High performance: Half slot provides a dissipation capacity of 700W, supporting 2 x 145W E5 v3 processors
Cost-effective large-memory: Provides 24 DIMMs at 1.5 times the usual height that apply mainstream granules to double capacity with a total of up to 1.5 TB DDR4 memory capacity (most cost-effective for large-memory applications)
Flexible PCIe expansion: support 1 standard FHHL PCIe card，users can choose proper PCIe acceleration solution for service optimization
Highlights
Notes: 448给个算法：14Gbps×32（两个连接器，32对serdes）
5.76T：16×36（32+4）

## Slide 7
CH220/CH221 product view
CH220 V3 Full Width IO Expansion Node
Front view
Isometric view
Strong expansion capability: support standard PCIe card, a maximum of 6 PCIe cards are supported in one full width slot, industry Leading PCIe expansion capability
High performance: full width slot provides a dissipation capacity of 1400W, adoption of 2 x FHFL GPU cards can greatly improve HPC application performance
Cost-effective large-memory: Provides 16 DIMMs at 1.5 times the usual height, most cost-effective for large-memory applications
Highlights
Form factor | Full-width 2-socket computing node
Number of CPUs | 1 or 2
Processor model | Intel Xeon E5-2600 v3 Series CPU
Number of DIMMs | 16 DDR4 DIMMs, providing a maximum capacity of 1TB
Number of HDDs | 2 x 2.5” SSDs or SAS/SATA HDDs, supporting 2 x PCIe SSDs
RAID support | Support RAID 0 and 1
PCIe expansion | 4 MEZZ modules (2 x PCIe x16 + 2 x PCIe x8) 6 STD. PCIe card slots: 4 x PCIe x8 FHHL and 2 x PCIe x16 FHFL
Operating systems supported | Microsoft Windows Sever 2008 /2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX
Operating temperatures | 5℃-40℃
Dimensions | 423 mm x 537.2mm x 60.46mm
Notes: Designed for application acceleration, VDI, virtualization and databases scenarios, the CH220 V3 provides superior scalability. Featuring Intel® Xeon® E5-2600 v3 series processors and support for up to 16 DIMM slots, 2 internal hard disks, and 6 standard PCI cards for various PCIe configurations, the CH220 V3 can be expanded for I/O acceleration components
such as PCIe SSDs, GPUs, and HPC acceleration components.
Provides 6 standard PCIe x16 full-height slots for supporting various PCIe configuration modes, including 6 full-height half-length single-slots, 1 full-height full-length dual-slot and four full-height half-length single slots, or 2 full-height full-length dual-slots. The cables to the 2 standard PCIe cards are routed from the front panel.
In addition, the CH220 v3 supports 24* 64 GB DIMMs at 1.5 times the usual height, providing a maximum capacity of 1 TB, and is most cost-effective for large-memory applications.

## Slide 8
CH222 product view
CH222 V3 Full-Width Storage Expansion Node
Ultra-Large storage: Full width slot provides 15 x 2.5 inch HDD bays, providing a maximum capacity of 18TB, very suitable for applications of big data and ServerSAN
Flexible PCIe expansion: support 1 standard FHHL PCIe card，users can choose proper PCIe acceleration solution for service optimization
Cost-effective large-memory: Provides 24 DIMMs at 1.5 times the usual height, most cost-effective for large-memory applications
Highlights
Form factor | Full-width 2-socket computing node
Number of CPUs | 1 or 2
Processor model | Intel Xeon E5-2600 v3 Series CPU
Number of DIMMs | 24 DDR4 DIMMs, providing a maximum capacity of 1.5TB
Number of HDDs | 15 x 2.5 inch SSDs or SAS/SATA HDDs
RAID support | Support RAID 0,1,10,5,50,6,60, 1GB RAID cache
PCIe expansion | 2 PCIe x16 MEZZ modules 1 PCIe x16 FHHL card
Operating systems supported | Microsoft Windows Sever 2008 / 2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX
Operating temperatures | 5℃-40℃
Dimensions | 423 mm x 537.2mm x 60.46mm
Front view
Isometric view
Notes: The CH222 v3 storage expansion node provides the most 2.5-inch hard disk bays in one full-width slot in the industry.
The CH222 v3 provides superior computing performance and a large storage capacity. Featuring Intel® Xeon® E5-2600 v3 series processors (up to 145 W) and support for up to 24 DIMM slots, 15 x 2.5" hard disks, and a 1 GB RAID cache, the CH222 V3 is suitable for big-data analysis and processing applications that require large storage capacity and high computing performance, such as videos, web searches, and biological sciences.
The CH222 v3 supports 24* 64 GB DIMMs at 1.5 times the usual height, providing a maximum capacity of 1.5 TB, and is most cost-effective for large-memory applications.

## Slide 9
CH220/CH221 product view
CH220 V3 Full Width IO Expansion Node
Front view
Isometric view
Strong expansion capability: support standard PCIe card, a maximum of 6 PCIe cards are supported in one full width slot, industry Leading PCIe expansion capability
High performance: full width slot provides a dissipation capacity of 1400W, adoption of 2 x FHFL GPU cards can greatly improve HPC application performance
Cost-effective large-memory: Provides 16 DIMMs at 1.5 times the usual height, most cost-effective for large-memory applications
Highlights
Form factor | Full-width 2-socket computing node
Number of CPUs | 1 or 2
Processor model | Intel Xeon E5-2600 v3 Series CPU
Number of DIMMs | 16 DDR4 DIMMs, providing a maximum capacity of 1TB
Number of HDDs | 2 x 2.5” SSDs or SAS/SATA HDDs, supporting 2 x PCIe SSDs
RAID support | Support RAID 0 and 1
PCIe expansion | 4 MEZZ modules (2 x PCIe x16 + 2 x PCIe x8) 6 STD. PCIe card slots: 4 x PCIe x8 FHHL and 2 x PCIe x16 FHFL
Operating systems supported | Microsoft Windows Sever 2008 /2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX
Operating temperatures | 5℃-40℃
Dimensions | 423 mm x 537.2mm x 60.46mm

## Slide 10
CH222 product view
CH222 V3 Full-Width Storage Expansion Node
Ultra-Large storage: Full width slot provides 15 x 2.5 inch HDD bays, providing a maximum capacity of 18TB, very suitable for applications of big data and ServerSAN
Flexible PCIe expansion: support 1 standard FHHL PCIe card，users can choose proper PCIe acceleration solution for service optimization
Cost-effective large-memory: Provides 24 DIMMs at 1.5 times the usual height, most cost-effective for large-memory applications
Highlights
Form factor | Full-width 2-socket computing node
Number of CPUs | 1 or 2
Processor model | Intel Xeon E5-2600 v3 Series CPU
Number of DIMMs | 24 DDR4 DIMMs, providing a maximum capacity of 1.5TB
Number of HDDs | 15 x 2.5 inch SSDs or SAS/SATA HDDs
RAID support | Support RAID 0,1,10,5,50,6,60, 1GB RAID cache
PCIe expansion | 2 PCIe x16 MEZZ modules 1 PCIe x16 FHHL card
Operating systems supported | Microsoft Windows Sever 2008 / 2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX
Operating temperatures | 5℃-40℃
Dimensions | 423 mm x 537.2mm x 60.46mm
Front view
Isometric view

## Slide 11
CH222 product view
CH226 V3 Full-Width Storage Expansion Node
Ultra-Large storage: Full width slot provides 2 x 2.5 inch and 6 x 3.5 inch HDDs, providing a maximum capacity of 36TB(6TB per disk), ideal for distributed databases and big data analysis.
Flexible PCIe expansion: support 1 standard FHHL PCIe card，users can choose proper PCIe acceleration solution for service optimization
High Reliability：Support stable operation at 40°C high temperature
Highlights
Form factor | Full-width 2-socket computing node
Number of CPUs | 1 or 2 Intel Xeon E5-2600 v3 Series CPU
Number of DIMMs | 24 DDR4 DIMMs, providing a maximum capacity of 1.5TB
Number of HDDs | 2 x 2.5 inch SSDs or SAS/SATA HDDs,6 x 3.5 inch SAS/SATA HDDs
RAID support | Support RAID 0,1,10,5,50,6,60, 1GB RAID cache
Internal Storage | 2 x Micro SD / 2 x SATA DOM / 1 x U-disk(USB 3.0)
PCIe expansion | 2 PCIe x16 MEZZ modules 1 PCIe x8 FHHL card
Operating systems supported | Microsoft Windows Sever 2008 / 2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX
Operating temperatures | 5℃-40℃
Dimensions | 423 mm x 537.2mm x 60.46mm
Front view
Isometric view
Notes: The CH222 v3 storage expansion node provides the most 2.5-inch hard disk bays in one full-width slot in the industry.
The CH222 v3 provides superior computing performance and a large storage capacity. Featuring Intel® Xeon® E5-2600 v3 series processors (up to 145 W) and support for up to 24 DIMM slots, 15 x 2.5" hard disks, and a 1 GB RAID cache, the CH222 V3 is suitable for big-data analysis and processing applications that require large storage capacity and high computing performance, such as videos, web searches, and biological sciences.
The CH222 v3 supports 24* 64 GB DIMMs at 1.5 times the usual height, providing a maximum capacity of 1.5 TB, and is most cost-effective for large-memory applications.

## Slide 12
CH240 product view
CH240 Full Width Computing Node
High performance: full width slot supports 4 E5-4600 or v2 processors and 48 DDR3 DIMMs, providing a maximum memory capacity of 3TB
Large storage: full slot provides 8 x 2.5 inch HDDs bays, suitable for database applications requiring both computing performance and local storage capacity
Cost-effective large-memory: Provides 48 DIMMs at 1.5 times the usual height, most cost-effective for large-memory applications
Highlights
Form factor | Full-width 4-socket computing node
Number of CPUs | 2 or 4
Processor model | Intel Xeon E5-4600 or E5-4600 v2 processors
Number of DIMMs | 48 DDR3 DIMMs, providing a maximum capacity of 3TB
Number of HDDs | 8 x 2.5 inch SSDs or SAS/SATA HDDs
RAID support | Support RAID 0,1,10,5,50,6,60, 512MB/1GB RAID cache
PCIe expansion | 2 PCIe x16 mezz modules
Operating systems supported | Microsoft Windows Sever 2008 /2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX ……
Operating temperatures | 5℃-40℃
Dimensions | 423 mm x 537.2mm x 60.46mm
Front view
Isometric view
Notes: 448给个算法：14Gbps×32（两个连接器，32对serdes）
5.76T：16×36（32+4）

## Slide 13
CH242 V3 product view
CH242 V3 Full Width Computing Node
High performance: full width slot supports 4 E7v2 or E7 v3 processors and 32 DDR3 or DDR4 DIMMs, supporting Max. Intel memory buffer width
Large storage: provides 8 2.5 inch HDDs bays, providing a maximum capacity of 14.4T, suitable for database applications requiring both computing performance and local storage capacity
Flexible PCIe expansion: support Max. 2 standard PCIe card，supporting GPU and PCIe SSD cards, suitable for large data sets and transaction-intensive database like HANA, Oracle DB etc. .
Highlights
Form factor | Full-width 4-socket computing node
Number of CPUs | 2 or 4 full series of Intel Xeon E7 v2, E7 v3,up to 18cores,165W
Number of DIMMs | E7 V2 processor:32 DDR3 DIMMs, 32 channels E7 V3 processor:32 DDR4 DIMMs, 32 channels
Number of HDDs | 8 or 4 2.5 inch SSDs or SAS/SATA HDDs
RAID support | Support RAID 0/1/10/5/50/6/60, 512MB/1GB RAID Cache
Internal Storage | 2 x Micro SD / / 1 x U-disk(USB 3.0)
PCIe expansion | 4 PCIe x16 mezz modules 2 PCIe x16 FHHL PCIe cards,
Operating systems supported | Microsoft Windows Sever 2008 / 2012 Red Hat Enterprise Linux SUSE Linux Enterprise Server Citrix XenServer VMware ESX
Operating temperatures | 5℃-40℃
Dimensions | 423 mm(16.65in.)*525mm(20.67 in.)*60.46mm(2.38 in.)
Front view
Top view
Notes: 448给个算法：14Gbps×32（两个连接器，32对serdes）
5.76T：16×36（32+4）

## Slide 14: Agenda
1
Click to add Title
Click to add Title
2
Huawei E9000 Server
Huawei E9000 IO System
Click to add Title
3
Configuration and Quotation Tool
Click to add Title
4
Demo

## Slide 15
Mapping Between MEZZ and Switch Slots
MEZZ and Switch Slots
Description
Mapping between MEZZ and switch slots
Blade
MEZZ 1
MEZZ 2
E1
X2
X3
E4
Switch slots
Computing nodes
Mezz1 is mapped to switch module slots 2 and 3.
Mezz2 is mapped to switch module slots 1 and 4.
Mezz module types must match switch modules. Two mezz modules can be flexibly configured with two pairs of switch modules.
Description
4E
1E
3X
2X

## Slide 16
E9000 High Backplane Connections
I/O Connectors
Specification
The three I/O connectors on the backplane for each half-width compute node are A, B, and C.
LAN on motherboard (LOM) uses connector A.
The upper mezz module in slot MEZZ1 uses connector B.
The lower mezz module in slot MEZZ2 uses connector C
The reserved LOM is fixedly connected to slots 2X and 3X. The backplane reserves two SerDes lanes for LOM signals to each slot.
MEZZ1 is fixedly connected to slots 2X and 3X The backplane reserves eight SerDes lanes for MEZZ1 signals to each slot.
MEZZ2 is fixedly connected to slots 1E and 4E The backplane reserves 8 SerDes lanes for MEZZ2 signals to each slot.
I/O Connections Specification
Backplane
半宽刀片
A
B
C
A
B
C
A: LOM
B: MEZZ1
C: MEZZ2
2X
3X
1E
4E
8x
A
B
C
Half-width Node
Mezz2
Mezz1
B
C
8x
8x
8x
Half-width Node
Full-width Node
Backplane
I/O Connections from MEZZ card to switch slot

## Slide 17
E9000 Switch Module
Switch Module
Switch Module
CX110
CX310
CX311
CX116
CX317
CX611
CX911/CX912
10GE / FCoE
IB QDR/FDR
10GE + FC
GE + FC
CX111
CX210
CX915
GE
10GE / FCoE
8G FC
16G FC
CX220
40GE
CX710
Enables data center TRILL large layer 2 network construction
Supports DCB lossless Ethernet to bear FCoE and iSCSI
Supports a converged network, virtual paths, and flexible Ethernet and FC configuration
Highlights
uplink: 12*GE and 4*10GE
downlink: 32*GE
uplink: 32*GE
downlink: 32*GE
uplink: 8*16G FC
downlink: 16* 16G FC
uplink: 16*10GE
downlink: 32*10GE
uplink: 32*10GE
downlink: 32*10GE
uplink: 18* FDR IB
downlink: 16*FDR IB
uplink: 16*10GE + 8*8GFC
downlink: 32*10GE and 16*8GFC
uplink: 8*8G FC
downlink: 16*8G FC
uplink: 16*GE + 8*8GFC
downlink: 32*GE and 16*8GFC
uplink: 12*GE and 4*10GE
downlink: 32*GE
uplink: 16*10GE + 8 *8G FC
downlink: 32*10GE
uplink: 8* 40GE
downlink: 16*40GE

## Slide 18
MEZZ Modules
MEZZ Modules
Models
Front view
Isometric view
Mainboard connecter
Backplane
highspeed connecter
Model
Description
Specification
GE | MZ110 | NIC mezz module with 4 x GE ports | 
10GE | MZ310 | ETH mezz module with 2 x 10GE ports | Use Intel 82599 chip,supports DPDK
 | MZ312 | ETH mezz module with 4 x 10GE ports | Use Intel 82599 chip,supports DPDK
 | MZ510 | CNA mezz module with 2 x 10GE ports | Supports FCoE, and FCoE supports NPIV and NPAR. A physical port can be split up to 4 NPARs.
 | MZ512 | CNA mezz module with 4 x 10GE ports | Supports FCoE, and FCoE supports NPIV and NPAR. A physical port can be split up to 4 NPARs.
40GE | MZ710 | 40GE ROCE mezz module with 2 x 40GE ports | Support ROCE
Multi-IO | MZ910 | FC mezz module with 2 x 10GE and 2 x 8G FC ports | FC ports support NPIV.
 | MZ912 | FC mezz module with 2 x 10GE and 2 x 8G FC ports | FC ports support NPIV.ETH use Intel 82599 chip, supports DPDK
InfiniBand | MZ610 | HCA mezz module with 2 x 4X InfiniBand QDR ports | 
 | MZ611 | HCA mezz module with 2 x 4X InfiniBand FDR ports | 
16G FC | MZ220 | FC mezz module with 2 x 16G FC ports | 
Type

## Slide 19: Mezz Card and Blade Compatibility Matrix
 Improvements of the CH220 V3 over the CH220 V1: Mezz cards and PCIe cards can be configured at the same time.
Blade Type | GE MEZZ Module | 10GE MEZZ Module |  | 40GE MEZZ Module | Multi-IO Mezz Module | InfiniBand Mezz Module | 
 | MZ110 | MZ510 | MZ512 | MZ710 | MZ910 | MZ610 | MZ611
CH121 V3 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz 2 | Mezz 2
CH220 V3 ① | Mezz1 /2/3/4 | Mezz1 /2/3/4 | Mezz2/3 | Mezz2/3 | Mezz1/2/3/4 | Mezz2/4 | Mezz2/4
CH222 V3 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz 2 | Mezz 2
CH242 V3 | Mezz1 /2/3/4 | Mezz1 /2/3/4 | Mezz1 /2/3/4 | Mezz1/2/3/4 | Mezz1 /2/3/4 | Mezz2/4 | Mezz2/4
CH240 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz1 /2 | Mezz 2 | Mezz 2

## Slide 20: Agenda
1
Click to add Title
Click to add Title
2
Huawei E9000 Server
Huawei E9000 IO System
Click to add Title
3
Configuration and Quotation Tool
Click to add Title
4
Demo

## Slide 21: UniSTAR
UniSTAR is a brand of configuration tool, including eDesigner, SCT and eCFG in EBG.
UniSTAR eDesigner
UniSTAR SCT
UniSTAR eCFG
A professional solution design tool, based on Web.
A Web-based smart configuration tool, provides a unified platform for all product lines of EBG.
Configuration tool client, used for offline quotation or special scenerios.
http://app.huawei.com/unistar/edesigner
http://www.huawei.com/sct
http://cfg.huawei.com: 8080/WebUI/index.jsp
Notes: http: //app.huawei.com/unistar/edesigner/solution.jsp
http: //app.huawei.com/unistar/sct
http: //cfg.huawei.com: 8080/WebUI/index.jsp

## Slide 22
What Is SCT
SCT is a Swift, Smart, and Simple online tool that makes configuration and quotation easier!
Quotation
Easily create quotations
Product
Browsing Huawei products
Simple discount setting
Automatic price verification
Hot-selling products
New products

## Slide 23
Applying for Permission
The SCT provides flexible service applications. The following examples describe a typical submitting order procedure.
If you have eCFG permission, use your W3 account to log in to the SCT.
If you do not have eCFG permission, apply for SCT permission using Huawei permission application e-flow.
Employees of Huawei's channel partner:
  Log in to Huawei's official website and apply for a Uniportal user account.
  Apply for associating with the Huawei channel partner‘s organization at User Information & Permission Management （UIPM） platform.
Huawei-certified partner
Huawei product manager
Administrators of Huawei's channel partner:
  Approve the applications for associating organizations on the UIPM.
  Submit the applications of applying for SCT permission for the employees on the UIPM.
  Select an enterprise product line, for example, Enterprise IP Product Line, from the Level 2 Function drop-down list.
  Select Product Data Package from the Level 1 Function drop-down list.

## Slide 24
Logging In to SCT
  Click User Login to log in as a registered user.
  Click Guest Login to log in to the SCT as a guest to browse and configure products.
  A guest can log in after entering the verification code.
 Note:
Recommended resolution ratio: 1280 x 1024.
Recommended browser: Internet Explorer 8.0+, FireFox 11.0+, Safari 5.12+, or Chrome19.0+.
Visit http://www.huawei.com/sct.

## Slide 25
Logging In to SCT
After login, select the country or area where you are located. Products that can be sold may vary based on your location.
  Click Change to change your location.
  Select a country or area.

## Slide 26: Agenda
1
Click to add Title
Click to add Title
2
Huawei E9000 Server
Huawei E9000 IO System
Click to add Title
3
Configuration and Quotation Tool
Click to add Title
4
Demo

## Slide 27
Create Quotation
Click ‘My Quotation’, system will load the ‘Draft’ page.
Click ‘New’ to create a new quotation.
Name this quotation and save.

## Slide 28
Add Product
In ‘Configure’ Page, click ‘Add Product’ button.
seach the needed product, select it and add to quotation.
NOTICE: please add blade server AND E9000 Chassis to quotation.
1
2
3
4
5
6

## Slide 29
Production Config Page
Click the config name in configuration list, the configuration page of this product will launch.
There are 3 kinds of product configuration status: Correct, Warning, Error. When the configuration status is Error, it will be held on and cannot continue to go ahead.
If you want to get the help information of an item, you can click the icon of its row.

## Slide 30
Configuring Product
In Product Parameter page, config all items one by one accourding to customer requirements.
Please remember to save it.
NOTICE: Mezz card of blade server should match with swich module of E9000 chassis in the same plane. Please get the detail information from the configuration help. This example configuration is CX310+MZ510.
E9000 Chassis
CH220 V3

## Slide 31
Configuring Service
After configuring product, go to Service Parameter page to config the service of this device, and save the modification.

## Slide 32
Double Confirm the Result
In Config Result page, you can double confirm the configuration result.
The manual modification on this page is NOT recommended.

## Slide 33
Go Back to Configuration List
If there are several configurations in this quotation, you can switch their configuration page by clicking their name in the configuration list.
After all configuratoin are completed, please click ‘Back to Configuration List of Quotation (Draft)’
Go back to configuration list of quotation
Configuration List

## Slide 34
Set sites and quantity
Set Sites
Model & Site Management
Set sites and quantities.

## Slide 35
Set INCOTERMS and discounts
Set INCOTERMS and discounts in step 3.

## Slide 36
Submit Quotation
In the last step, you can submit this quotation.
If you need other sct users to help completing the quotaiton, you can share this quotation to him(her).
You can expert BOQ and show it to customer.