## Slide 1: LS-DYNA Performance Benchmark and Profiling
October 2017

## Slide 2: Note
The following research was performed under the HPC Advisory Council activities
  Participating vendors: LSTC, Huawei, Mellanox
  Compute resource - HPC Advisory Council Cluster Center
The following was done to provide best practices
  LS-DYNA performance overview
  Understanding LS-DYNA communication patterns
  Ways to increase LS-DYNA productivity
  MPI libraries comparisons
For more info please refer to
  http://www.lstc.com
  http://www.huawei.com
  http://www.mellanox.com

## Slide 3: LS-DYNA
LS-DYNA
  A general purpose structural and fluid analysis simulation software package capable of simulating complex real world problems
  Developed by the Livermore Software Technology Corporation (LSTC)
LS-DYNA used by
  Automobile
  Aerospace
  Construction
  Military
  Manufacturing
  Bioengineering

## Slide 4: Objectives
The presented research was done to provide best practices
  LS-DYNA performance benchmarking
    MPI Library performance comparison
    Interconnect performance comparison
    Compilers comparison
    Optimization tuning
The presented results will demonstrate
  The scalability of the compute environment/application
  Considerations for higher productivity and efficiency

## Slide 5: Test Cluster Configuration
Huawei FusionServer E9000 with FusionServer CH121 V5 16-node (640-core) “Skylake” cluster
  Dual-Socket 20-Core Intel Xeon Gold 6138 @ 2.00 GHz CPUs
  Memory: 192GB memory, DDR4 2666 MHz RDIMMs per node
  OS: RHEL 7.2, MLNX_OFED_LINUX-4.1-1.0.2.0 InfiniBand SW stack
Mellanox ConnectX-5 EDR 100Gb/s InfiniBand Adapters
Mellanox Switch-IB SB7800 36-port EDR 100Gb/s InfiniBand Switch
Compilers: Intel Parallel Studio XE 2018
MPI: Intel MPI 2018, Mellanox HPC-X MPI Toolkit v1.9.7, Platform MPI 9.1.4.3
Application: MPP LS-DYNA R9.1.0, build 113698, single precision
MPI Profiler: IPM (from Mellanox HPC-X)
Benchmarks: TopCrunch benchmarks
  Neon Refined Revised (neon_refined_revised), Three Vehicle Collision (3cars), NCAC Minivan Model (Caravan2m-ver10), odb10m (NCAC Taurus model)

## Slide 6: Introducing Huawei FusionServer E9000 (CH121) V5
High-Performance 2-Socket Blade Unlocks Supreme Computing Power
Full-series Intel® Xeon® Scalable Processors, 24 DDR4 DIMMs, AEP memory supported, 1 PCIe slot, 2 SFF/2 NVMe SSDs/4 M.2 SSDs high-performance storage, multi-plane network, LOM supported

## Slide 7: LS-DYNA Performance – CPU SKUs and Generation
LS-DYNA performance gain by larger core counts and better memory throughput
  The “Gold 6140” demonstrates a 50% of performance gain (29% more cores) vs E5-2680v4
  The “Gold 6148” demonstrates a 61% of performance gain (42% more cores) vs E5-2680v4
  Base clock are the same on E5-2680 v4 and Gold 6148, while Gold 6140 runs slightly slower
  Skylake supports 6 memory channels and faster DIMMs which impacts on memory performance
Single Node Performance
Higher is better
61%
50%
Notes: 7

## Slide 8: LS-DYNA Performance – Memory Speed
Memory speed provides some benefits to LS-DYNA performance
  Skylake platform supports DIMM speed up to 2666MHz DIMMs
  2666MHz DIMMs is theoretically ~11% faster than the 2400MHz DIMMs
  LS-DYNA reports only about 2% of the improvement on a single node
  It appears only part of the speed difference is translated into LS-DYNA performance gain
40 MPI Processes / Node
Higher is better
Notes: 8

## Slide 9: LS-DYNA Performance – Sub-NUMA Clustering
Enabling SNC provides some benefits for LS-DYNA
  Sub-NUMA Clustering (SNC) is similar to a cluster-on-die (COD) in Haswell/Broadwell generation
  CPU cores and memory would be split into 2 separate NUMA domains when SNC is enabled
  SNC generally should demonstrate some benefits for applications that requires good NUMA locality
  SNC demonstrates a performance gain of 3% on a single node basis
40 MPI Processes / Node
Higher is better
Notes: 9

## Slide 10: LS-DYNA Performance – CPU Instructions
AVX2 outperforms both AVX-512 and SSE2 executables on Skylake CPU
  Performance gain of 17% by using AVX2 over AVX-512 executables
  AVX-512 performs worse compared to AVX2, despite improved vectorization
  AVX-512 instructions runs at a reduced clock frequency as AVX2 and normal clocks
  Benefit of AVX2 appears to be larger on bigger dataset (such as car2car)
40 MPI Processes / Node
Higher is better
17%
8%
4%
3%
Notes: 10

## Slide 11: LS-DYNA Performance – CPU Instruction Sets
Some variance in performance among different LS-DYNA versions/executables
  AVX2 performs better than SSE2 LS-DYNA executables
  Small variance in performance among different LS-DYNA releases
  R7.1.3 appeared to perform better on larger datasets
40 MPI Processes / Node
Higher is better
20%
Notes: 11

## Slide 12: LS-DYNA Performance – MPI Libraries
All three MPI implementations shows decent performance at scale
  Platform MPI and HPC-X performs similarly, while Intel MPI shows a drop at small dataset at scale
40 MPI Processes / Node
Higher is better
Notes: 12

## Slide 13: LS-DYNA Performance – System Generations
Current Skylake system configuration outperforms prior system generations
  Skylake platform outperformed Broadwell by 21%, Haswell by 51%, Ivy Bridge by 89%, Sandy Bridge by 132%, Westmere by 222%, Nehalem by 425%
  Skylake performs 41% better than Broadwell for the 3cars model on a single-node basis
  System components used:
    Skylake: 2-socket 20-core Xeon Gold 6138 2.0GHz, 2666MHz DIMMs, ConnectX-5 EDR InfiniBand
    Broadwell: 2-socket 14-core Xeon E5-2690v4 2.6GHz, 2400MHz DIMMs, ConnectX-4 EDR InfiniBand
    Haswell: 2-socket 14-core Xeon E5-2697v3 2.6GHz, 2133MHz DIMMs, ConnectX-4 EDR InfiniBand
    Ivy Bridge: 2-socket 10-core Xeon E5-2680v2 2.8GHz, 1600MHz DIMMs, Connect-IB FDR InfiniBand
    Sandy Bridge: 2-socket 8-core Xeon E5-2680 2.7GHz, 1600MHz DIMMs, ConnectX-3 FDR InfiniBand
    Westmere: 2-socket 6-core Xeon x5670 2.93GHz, 1333MHz DIMMs, ConnectX-2 QDR InfiniBand
    Nehalem: 2-socket 4-core Xeon x5570 2.93GHz, 1333MHz DIMMs, ConnectX-2 QDR InfiniBand
Best results shown
Higher is better
41%
Notes: 13

## Slide 14: LS-DYNA Summary
LS-DYNA is multi-purpose explicit and implicit finite element program
  Utilizes both compute and network communications
MPI library performance
  Platform MPI and HPC-X performs similarly, while Intel MPI shows a drop at small dataset
Effect on CPU instructions
  AVX-512 performs worse compared to AVX2, despite improved vectorization
  AVX-512 instructions runs at a reduced clock frequency as AVX2 and normal clocks
Effect on CPU cores per node
  Almost no difference when limiting the number of CPUs per node from 40 to 36 or 32
Effect on LS-DYNA versions
  Small variance in performance among different LS-DYNA releases

## Slide 15
15
Thank You
HPC Advisory Council
All trademarks are property of their respective owners. All information is provided “As-Is” without any kind of warranty. The HPC Advisory Council makes no representation to the accuracy and completeness of the information contained herein. HPC Advisory Council undertakes no duty and assumes no obligation to update or correct any information presented herein